## Slide 1: Sample Application
COMIF
CDU Interface
Aircraft Interface
AFDS
(Autopilot Flight Director System)
Flight Dynamic Model (FDM)
Aircraft flight simulation (lat, long, alt, heading, roll, pitch, etc.)
NAV Interface
NAV
(Waypoint Navigation)
GCAS
(Ground Collision Avoidance System)
CDU
(Control & Display Unit)
AFDS Interface
GCAS Interface

## Slide 2: Components
Each component follows the same pattern
  A component XYZ is made of two parts:
    Data interface: XYZ.iface and XYZ.iface.*
    The implementation: XYZ and XYZ.*
  The XYZ package contains the single entry point for the component: ‘step’
  A step is made of 3 actions
    Read data from the global interface (IF.* packages) to the local interface (XYZ.iface.*)
    Perform the function(s) of the component
    Write data back from the local interface (XYZ.iface.*) to the global interface (IF.*)
  For example, AFDS step subprogram is:
procedure step is
begin
AFDS.iface.read; -- read data from all relevant interfaces
AFDS.GCAS.step;
AFDS.heading.step;
AFDS.altitude.step;
AFDS.velocity.step;
AFDS.vspeed.step;
AFDS.roll.step;
AFDS.pitch.step;
AFDS.iface.write; -- write data to all relevant interfaces
end step;

## Slide 3: COMIF
Components Interface

## Slide 4: Components communication
AFDS (Ada)
AFDS-*
autopilot
AFDS-IFACE
Data Input
AFDS-IFACE
Data Output
GCAS Interface
Aircraft Interface
NAV Interface
Aircraft Interface
NAV (C)
NAV-*
navigation
NAV-IFACE
Data Input
NAV-IFACE
Data Output
Aircraft Interface
NAV Interface
NAV Interface
…
AFDS Interface
AFDS Interface
Each component read and write data from to the other components via COMIF
  First, the required component data is read from COMIF in a local copy via the ‘iface’ package (e.g. AFDS.iface)
  Then, the component function is executed (potentially modifying the local copy of another component data).
  Finally, the required component data is written back to COMIF

## Slide 5
GCAS
COMIF
AFDS
GCAS.iface.aircraft
GCAS.iface.GCAS
COMIF.aircraft
COMIF.GCAS
COMIF.GCAS
GCAS.step
GCAS.iface.GCAS
AFDS.iface.aircraft
AFDS.iface.AFDS
AFDS.iface.NAV
AFDS.iface.GCAS
COMIF.aircraft
COMIF.AFDS
COMIF.NAV
COMIF.GCAS
COMIF.aircraft
COMIF.AFDS
AFDS.step
AFDS.iface.aircraft
AFDS.iface.AFDS

## Slide 6: COMIF allowed data paths
 | Aircraft status | Aircraft control | AFDS | GCAS | NAV | CDU
AFDS | R | RW | RW | R | R | -
GCAS | R | - | - | RW | - | -
NAV | R | - | - | - | RW | -
CDU | - | - | RW | RW | RW | RW
FDM | RW | RW | - | - | - | -
TEST | RW | RW | RW | RW | RW | RW

## Slide 7: GCAS
Ground Collision Avoidance System

## Slide 8: GCAS
The GCAS component detect potential ground collision and set the GCAS state accordingly (see next slide)
The GCAS state is checked by the AFDS component and the AFDS.GCAS function of this component implements the required manoeuvre.

## Slide 9
GCAS
GCAS-IMPL
GCAS-IFACE
Data Input
GCAS-IFACE
Data Output
GCAS Interface
Aircraft Interface
GCAS Interface
disengaged
emergency
recovery
stabilize
Collision predicted
Vertical speed > threshold
Altitude > threshold
Stable flight
(Pitch, Roll, Velocity)
Collision predicted
Collision predicted

## Slide 10: AFDS
Automatic Flight Director System

## Slide 11: AFDS
The AFDS read the current and desired heading, altitude and velocity set by the AFDS, NAV or CDU components and calculate the require commands for the aileron, elevator, rudder and throttle.
The AFDS.GCAS can override the NAV input to force an emergency collision avoidance manoeuvre.

## Slide 12: AFDS-* (Autopilot)
Altitude
Heading
Velocity
Aircraft
status
NAV
settings
Pitch
Roll
Ailerons
Vertical Speed
Elevators
Throttles
Aircraft
control
Rudder

## Slide 13
Altitude
Heading
Velocity
Aircraft
status
NAV
settings
Pitch
Roll
Ailerons
Vertical Speed
Elevators
Throttles
Aircraft
control
Rudder
AFDS-GCAS
AFDS-GCAS override
GCAS
status

## Slide 14: NAV
(Waypoint) Navigation

## Slide 15: NAV
This component is implemented in C
The NAV component navigate to the next waypoint.
When a waypoint is reached, the next waypoint in the list is selected as the active waypoint.
Navigation data (desired heading, altitude, velocity) are written to the IFACE.NAV interface for the AFDS component to read.

## Slide 16: CDU
Control & Display Unit

## Slide 17: CDU
The CDU component can:
  Enable/Disable GCAS, AFDS and NAV
  NAV:
    Clear the NAV waypoint list
    Add a waypoint list
  AFDS
    Set the desired navigation target
The CDU component receives
  The state of GCAS, AFDS and NAV (enabled/disabled)