## Slide 1: Application
GCAS
(Ground Collision Avoidance System)
AFDS
(Autopilot Flight Director System)
NAV
(Waypoint Navigation)
GCAS Interface
Aircraft Interface
override
config
Flight Dynamic Model (FDM)
Aircraft flight simulation (lat, long, alt, heading, roll, pitch, etc.)
NAV Interface

## Slide 2: Components
Each component follows the same pattern
  A component XYZ is made of two parts:
    Data interface: XYZ.iface and XYZ.iface.*
    The implementation: XYZ and XYZ.*
  The XYZ package contains the single entry point for the component: ‘step’
  A step is made of 3 actions
    Read data from the global interface (IFACE.* packages) to the local interface (XYZ.iface.*)
    Perform the function(s) of the component
    Write data back from the local interface (XYZ.iface.*) to the global interface (IFACE.*)
  For example AFDS step subprogram is:
procedure step is
begin
AFDS.iface.read; -- read data from all relevant interfaces
AFDS.GCAS.step;
AFDS.heading.step;
AFDS.altitude.step;
AFDS.velocity.step;
AFDS.vspeed.step;
AFDS.roll.step;
AFDS.pitch.step;
AFDS.iface.write; -- write data to all relevant interfaces
end step;

## Slide 3
AFDS (Ada)
AFDS-*
autopilot
AFDS-IFACE
Data Input
AFDS-IFACE
Data Output
GCAS Interface
Aircraft Interface
NAV Interface
Aircraft Interface
GCAS (Ada)
GCAS-*
GCAS-IFACE
Data Input
GCAS-IFACE
Data Output
GCAS Interface
Aircraft Interface
GCAS Interface
NAV (C)
NAV-*
navigation
NAV-IFACE
Data Input
NAV-IFACE
Data Output
Aircraft Interface
NAV Interface
NAV Interface

## Slide 4
AFDS
AFDS.iface
IFACE
IFACE.aircraft
IFACE.GCAS
IFACE.NAV
AFDS. iface. aircraft
AFDS. iface. GCAS
AFDS. iface. NAV
AFDS.* AFDS function implementation
GCAS
GCAS.iface
GCAS. iface. aircraft
GACS. iface. GCAS
GCAS.* GACS function implementation
NAV
NAV.iface
NAV. iface. aircraft
NAV. iface. NAV
NAV.* NAV function implementation

## Slide 5: GCAS

## Slide 6: GCAS
The GCAS component detect potential ground collision and set the GCAS state accordingly (see next slide)
The GCAS state is checked by the AFDS component and the AFDS.GCAS function of this component implements the required manoeuvre.

## Slide 7
GCAS
GCAS-IMPL
GCAS-IFACE
Data Input
GCAS-IFACE
Data Output
GCAS Interface
Aircraft Interface
GCAS Interface
disengaged
emergency
recovery
stabilize
Collision predicted
Vertical speed > threshold
Altitude > threshold
Stable flight
(Pitch, Roll, Velocity)
Collision predicted
Collision predicted

## Slide 8: AFDS

## Slide 9: AFDS
The AFDS read the current and desired heading, altitude and velocity set by the NAV component and calculate the require commands for the aileron, elevator, rudder and throttle.
The AFDS.GCAS can override the NAV input to force a emergency collision avoidance manoeuvre.

## Slide 10: AFDS-* (Autopilot)
Altitude
Heading
Velocity
Aircraft
status
NAV
settings
Pitch
Roll
Ailerons
Vertical Speed
Elevators
Throttles
Aircraft
control
Rudder

## Slide 11
Altitude
Heading
Velocity
Aircraft
status
NAV
settings
Pitch
Roll
Ailerons
Vertical Speed
Elevators
Throttles
Aircraft
control
Rudder
AFDS-GCAS
AFDS-GCAS override
GCAS
status

## Slide 12: NAV

## Slide 13: NAV
This component is implemented in C
The NAV component navigate to the next waypoint.
When a waypoint is reached, the next waypoint in the list is selected as the active waypoint.
Navigation data (desired heading, altitude, velocity) are written to the IFACE.NAV interface for the AFDS component to read.